Design and Simulation of Virtual Telephone Keypad Control Based on Brain Computer Interface (BCI) with Very High Transfer Rates

Rehab B. Ashari

Information systems Department
King ABdulaziz University
2002 Battlecreek Drive

Fort Collins, CO 80528

(303)931-3731

Rehab_ashary@yahoo.com

Ibrahim A. Al-Bidewi

Information systems Department
King ABdulaziz University
P.O. Box 80221, Jeddah  21589,

Saudi Arabia

(+966) 555500252

ialbidewi@hotmail.comMahmoud I. Kamel

Information systems Department
King ABdulaziz University
P.O. Box 80221, Jeddah  21589, Saudi Arabia

(+966)502570157

mahmodkamel@hotmail.com

ABSTRACT

Brain Computer Interface (BCI) is a communication and control mechanism which does not rely on any kind of muscular response to send a message to the external world. This technique is used to help paralyzed people with spinal cord injury to have the ability to communicate with the external world. In this paper we emphasize increasing the BCI System bit rate to control  a virtual telephone keypad. To achieve the proposed algorithm, a simulated virtual telephone keypad based on the Steady State Visual Evoked Potential (SSVEP) BCI system is developed. A Dynamic programming technique with the specifically modified Longest Common Subsequence (LCS) algorithm is used. By comparing the paralyzed user's selection with the previous selections which are stored records in the file of the telephone, the user can save the rest of his choices for controlling keypad, hence improving the overall performance of the BCI system. This axiomatic approach,  used in searching web pages for increasing the performance of searching, is more important  for a paralyzed person rather than a normal user.

Keywords

Brain Computer Interface, Steady State Visual Evoked Potential, Dynamic Programming, Longest Common Subsequence.

# INTRODUCTION

Brain Computer Interface (BCI) is a communication and control channel, that is based on direct measurement of brain activity rather than the physical movement by interfacing brain signals to the computer and translating brain electrical activities into messages or commands. This can be used in several computer applications such as spelling, cursor control, games and virtual environment control, which will be useful and helpful for patients who are severely paralyzed.

# LITERATURE REVIEW

Current BCI systems relatively low bandwidth devices, offering maximum information transfer rates of 5-25 bits/min at best, which may take several minutes to input simple word to computer. In addition BCI systems are error prone with a rate of 10 % to 30 % for either a false positive error, which refers to selecting the incorrect choice or a false negative error which refers to missing the correct choice. For both error types, BCI systems need error detection with error recovery and correction techniques to handle these errors [7, 13].

In 2002, Ming Cheng, Xiaorong Gao, Shangkai Gao, and Dingfeng Xu presented a Brain Computer Interface based on Steady State Visual Evoked Potential (SSVEP). It was displayed as a virtual telephone keypad on the computer monitor with thirteen buttons represented as ten digits (0-9), BACKSPACE, ENTER and on/off, each button having a different frequency. Users enter their required phone number by looking at these buttons, and every time users need to call the phone number they have to choose all the digits of the desired number. They used SSVEP in the BCI since it is recording a non-invasive signal, which eliminates the need for intensive training to use, and it has a high information transfer rate which was 27.15 bits/min, an average for all subjects [13, 14].

A. Materka and M. Byczuk have demonstrated how to increase the speed and accuracy of brain computer interface by proper selection of the stimulus frequency in SSVEP BCI systems, and by using COMB filtering of the EEG signal prior to performing the Discrete Fourier Transform (DFT) with a substantial increase of the SSVEP signal to noise ratio [15]. They investigated that the benefits of using COMB filtering is to suppress noise and artifacts whose spectral components do not coincide with the stimulus fundamental frequency and its harmonics. COMB filtering is a well known technique for luminance and chrominance components separation in color TV decoders and helps to separate the color signals from the black and white, providing a higher resolution or sharper picture. In this BCI they use the same idea of the virtual telephone key and they described five different layers, which are EEG acquisition, Pre-processing, Windowing FFT, Post processing and Analysis, and SSVEP Detection.

In 2005, Luca Piccini, Sergio Parini, Luca Maggi and Giuseppe Andreoni presented a wearable BCI system, which consists of two parts: The first one is the hardware, which they called Kimera, that consists of two layers of hardware architecture, wireless acquisition and transmission board based on Bluetooth arm chip, and a low power miniaturized biosignal acquisition analog front end. The second part of the system is the software, which they call Bellerophonte for the graphical user interface management, protocol execution, data recording, transmission and processing [16]. The implementation of this BCI system is based on SSVEP applied to two state selections using a standard monitor with a couple of high efficiency frequency LEDs. EEG signals are recorded from the O1 and O2 electrodes according to the 10-20 International System of electrodes placement. BCI system is based on supervised classifier implemented through a multi- class Conical Discriminate Analysis (CDA) with continuous real time feedback and requires a proper initial training period, which consists of nine phases of fifteen seconds equally distributed among three stimulus: Screen center fixation (NULL event), left stimulus (command A) and right stimulus fixation (command B).

In 2006, L. Maggi, S. Parini, G. Panfili and G. Andreoni presented a similar technology as previously presented by the Kimera and Bellerophone system, but with four commands instead of only two commands (up, down, left and right). This BCI system algorithm was based on a supervised multi class classifier implemented by combining different binary Regularized Linear Discriminate Analysis (RLDA) classifiers [17]. It is also a system based on a supervised translation algorithm, and a protocol consisting of three main functioning modes, which are training mode, meta-training mode and testing mode. After testing the system on five healthy subjects, the system showed good robustness against false positive and achieved accuracy during meta-training between 80 wth 100% and the average speed of 10-15 commands per minute. As a result of these findings, this BCI system provided a reliable, smart and low cost BCI system.

In 2006, Kim Dremstrup Nielsen, Alvaro Fuentes Cabrera, and Omar Feix do Nascimento described the BCI system based on SSVEP, which studied seven healthy subjects using a 3 X 3 matrix of flickering squares numbered from 1 to 9. Stimulation frequencies used were 5.0, 7.08, 7.73, 8.5, 10.63, 12.14, 14.16, 17.0 and 9.44 Hz in order for each box 1 to 9. They were displayed on a CRT computer screen with a refresh rate of 85 Hz. Subjects were instructed to enter their phone number, birth date and numbers from one to nine by focusing their gaze on the appropriate squares on the computer screen. Each phone number or birth date was selected three times, while numbers from one to nine were selected four times [18]. Online extraction of SSVEP features classification which is done using Fast Fourier Transform (FFT) based on non-averaged periodograms of 2048 samples. Symbol selection is based on first, second and third harmonics. If the amplitude is below a defined threshold, it means no symbol is selected. The result extracted from seven subjects showed 79.7% of the trials were correctly detected with a resulting signal rate of 9.3 characters per minute.

In 2007, Ola Friman, Thorsten Luth, Ivan Volosyak and Axel Graser presented on online spelling BCI application based on SSVEP, which displayed to the user with two different layouts, the raw column layout and the rhombus lay out. Both layouts were tested on eleven healthy subjects to spell the word BRAINCOMPUTERINTERFACE, which in previous off line studies was shown significantly improved classification performance [19]. The average information rate of this on-line spelling application was 27 bits/minute and the probability of correctly classifying the user’s attention was estimated to be 97.5%.

Gernot R. Muller-Purtz and Gert Pfurtscheller presented a 2-axis hand prosthesis, asynchronously (self-based) controlled with 4 class SSVEP based BCI. The hand prosthesis attach with four red lights(LED) at the fingers with the with the index finger to turn right, fifth finger to turn left and at the forearm there are two lights – the first one to open the hand and the second one to close it. All these lights flicker continuously with different frequencies 6, 7, 8 and 13 Hz [20]. The accuracy of the online classification for this BCI system was between 44 and 88%.

Zhonglin Lin, Chagshui Zhang, Wei Wu and Xiaorong Goe introduced canonical correlation analysis (CCA) to analyze the frequency component of the SSVEP in EEG. They employed CCA to extract frequency features in EEG, as well as to select channels for analysis. After that, the recognition strategy for SSVEP based BCI was proposed [21]. After testing this system, they concluded that the used signals in the PSDA approach had a very high SNR and the area that generated the SSVEP was very small, while the use of a signal within a broader area in the CCA approach can introduce more noise and negatively effect recognition accuracy.

Tilmann Kluge and Manfred Hartmann proposed a different estimator for the analysis of SSVEPs. In contrast to previously published Power Spectral Density (PSD) estimator, which is non-coherent measures for the signal power in narrow frequency band. In this study, they presented a phase coherent estimate that takes into account both amplitude and phase of Fourier series coefficients. The EEG signal was recorded from two electrodes and the used band-pass filter between 0.3Hz and 100Hz and a notch filter at 50Hz. Analog to digital conversion was performed using a data acquisition card with a sampling rate of 256Hz and 6 bit resolution [22]. In this approach, three different experiments were performed, such as two stimuli flickering with two different reversal rates ,two stimuli flickering both at 10 Hz, but with a different relative phase and Similar to the second one but stimuli flickered at 12Hz and the phase difference was 180 degrees.

In 2007, Ola Friman, Ivan Volosyak and Axel Graser presented six different methods: Average Combination, Native Combination, Bipolar Combination, Laplacian Combination, Minimum Energy Combination and Maximum Contrast Combination for detecting steady state visual evoked potentials, using multiple EEG signals for achieving high information transfer rates with high detection accuracy by finding combinations of electrode signals that cancel strong interference signal in EEG data [23]. The best detection accuracy was achieved with the minimum energy method, which utilized an SSVEP model to produce uncorrelated channels containing minimal energy from nuisance signals.

In all of the above BCI SSVEP systems, the transfer rates did not increase more than 27 bit/sec. This paper presented a simulated BCI system which is based on the SSVEP to increase the transfer rate compared with the A. Materka and M. Byczuk idea.

# PROPOSED SYSTEM

The block diagram of the BCI system, which is proposed and simulated in this paper, is shown in (see Figure 1).

## Software Layout

There are thirteen buttons: 0-9 buttons, the "Back" button to delete the wrong selection, the "Enter" button to signal the end of the user selections which will be automatically added to the telephone file if it was not found in the stored file and the "on/off" button that must be selected to start dialing his/her telephone number. All of these thirteen buttons have different frequencies and colors based on the SSVEP frequencies limitation starting from 4Hz to 35 Hz. The user selection field in the layout is to display the selection for the user and there is a signal result field to display the result of the user selection after applying all methods and algorithms on the selected button’s frequency.

## System Workflow

Presented BCI system worked as follow:

- First, the user has to select on/off button to start, and select his /her telephone number, this step will eliminate the false positive error (Selecting incorrect choice).

- Then, the user starts to dial the telephone number by selecting his/her selections from the telephone keypad.

- After that, the signal simulation takes place, which generates the first, second, and third harmonics of the selected button frequency as a summation of the three sin waves for the three harmonics, add power supplier 60Hz noise.

- Then work with the simulated signal as an EEG signal and clean that simulated signal from power noise by applying notch filter and transformed to the frequency domain using Fast Fourier Transform (FFT), then the correct frequency is extracted by getting the peak of the frequencies.

- Once the user has selected three digits or more, the system starts searching in the stored telephone user file to find the telephone numbers matching the same user (starting) digits using Dynamic Programming technique and the specially updated Longest Common Subsequence algorithm and displays the results to the user which will help the user to reach their desired telephone number faster with less selection.

- User has a chance to eliminate the number of matches from the file by selecting more digits from the telephone keypad.

- If the matches list is more than 20 records another screen will be shown with the new matches number with different frequencies.

- In case the user enters a wrong selection, he/she can select the Back button, which deletes the previous selection.

- Finally, if the user enters all the telephone number digits and system did not find it in the stored file, he/she can choose the Enter button and the telephone number will be stored in the file. This will then help the user to find the same number in a faster way. The next time the user will search for it then dial it.

# Results and Discussion

The presented BCI system contains thirteen buttons with different frequencies assigned to each button from 4-35 Hz. It is based on SSVEP (See Table 1) and it is displayed to the user once he/she start the program .

Note that frequencies assigned to the thirteen buttons internally in the program are within the range between 4Hz-16Hz. Matching phone numbers from the file are assigned to random frequencies between 17Hz– 35Hz excluding 34Hz  and 35Hz which are assigned to the "back" and "enter" buttons if the matching phone numbers from the file have more than 20 records.

From the hardware viewpoint, (see figure (2,3,4)) simulate the EEG signals in the frequency Domain, as well as, the addition of power line artifacts with its Notch filter.

Figures (2-9) show the simulated systems with the associated results.

Table 1. Buttons frequency

| Button | Assigned Frequency |
| --- | --- |
| On/Off | 5Hz |
| 0 | 4Hz |
| 1 | 6Hz |
| 2 | 7Hz |
| 3 | 8Hz |
| 4 | 9Hz |
| 5 | 10Hz |
| 6 | 11Hz |
| 7 | 12Hz |
| 8 | 13Hz |
| 9 | 14Hz |
| BackSpace | 15Hz |
| Enter | 16Hz |
| Results (Updated LCS) | 16Hz<Frequency<36Hz |

Figure 2. The original signal in the frequency domain obtained from EEG(O1&O2) due to a specific button.

Figure 3. The original signal corrupted with 60 Hz power supply noise.

Figure 4. The signal after applying the Notch filter.

- Find the Phone Number in the File

- Once user selects three or more digits, the system starts to search in the stored file for a match with the same start digits by dynamic programming technique, using Updated Longest Common Subsequence algorithm. Each result record assigned to special frequency between 17Hz-35Hz excluding 34Hz and 35Hz for "back" and "next" buttons if the result records are more than 20 records. First telephone keypad screen keep open to the user to give an ability to the user to shrink the number of resulted records by selecting more digits from the main screen buttons (See Figure ( 5,6,7, 8)).

- Each selected number goes through the same cycle, that was mentioned previously, but with different frequencies depending on the user selection.

- The user selects one of the retrieved results (each result referred to special frequency between 17Hz and 33Hz) that the system recognized based on the selection number, which helps the user to call the desired phone number faster and with a minimal number of selections, rather than entering all phone number digits every time the user wants to dial the same number.

- New Record in the File

In this case the user enters the first three digits of the desired phone number and cannot find it in the file, the result will be extracted as follows:

- User has to select all telephone number digits.

- User has to select enter button (frequency = 16Hz) to add this record in the file (See Figure (9,10))

- Telephone number is stored in the file and it will be available in the next time if the user wants to select the same number.

Figure 5. User selects 6, 2 and system recognize the Selection 6= 11Hz, 2=7Hz.

Figure 7. Matching phone number in Microsoft access

view.

Figure 8. Number of Results Eliminate Once User Enter More Digits.

Figure 9.  User selects "enter" to add the record to the file

|  | Previous Study | Current Study |
| --- | --- | --- |
| BCI based on | SSVEP | SSVEP |
| Number of Electrodes | Two electrodes O1,O2 | Two electrodes O1,O2 |
| Application Layout | On/Off 0-9 number backspace (wrong entry) Enter (end of selection) | On/Off 0-9 number backspace (wrong entry) Enter (end of selection & enter phone number in the file if it is not available before) |
| Telephone Filing | Not Available | A Available and display matches numbers to the user as a new button with different frequencies depending on the first three digits (at least) which were entered from the user. |
| Number of the selections ( first time) | All telephone number digits | All telephone number digits |
| Number of selections (same number in the second times) | All telephone number digits | First three digits. Select from the stored number in the file (in the second time it will be available in the file since it was stored after user selected in the first time) Number of Selections=4 |
| Transfer rate | Slower (More selections) | Faster (less selections) |

# CONCLUSION

This paper has presented a BCI system based on SSVEP displayed as a virtual telephone keypad in a GUI layout. This allows the user to select their desired phone number faster with a fewer number of entries due to a special telephone number file that is stored based on the user's previously dialed telephone numbers. The telephone numbers retrieved from the file were based on at least the first three digits entered by the user, and this matching list decreased once the user starts selecting more digits from his/her desired phone number. The system was implemented using  a dynamic programming technique with the updated Longest Common Subsequence algorithm constraint on at least the first three digits of the desired phone number and begins  matching data in the file and displays the matching list to the user as  buttons with different frequencies. Compared to the previous study, this paper reached user requirements faster with a fewer number of selections, which increased transfer rate.

# REFERENCES

[1] Gerhardt, G. A., WTEC Brain Computer Interface (BCI) Workshop: Sensor Technology. WTEC Workshop, University of Kentucky Health Sciences Center, 2006.

[2] Bashashati, A., Fatourechi, M., Ward, R. K. & Birch, G. E., A Survey of Signal Processing Algorithms in Brain-Computer Interfaces Based on Electrical Brain Signals, Journal of Neural Engineering, R32-R48, 2007.

[3] Wolpaw, J. R., Birbaumer, N., Mcfarland, D. J., Pfurtschellere, G. & Vaughana, T. M., Brain - Computer Interfaces for Communication and Control. Clinical Neurophysiology, 767- 791, 2002

[4]  Wolpaw, J. R., Birbaumer, N., Heetderks, W. J., Mcfarland, D. J., Peckham, P. H., Schalk, G., Donchin, E., Quatrano, L. A., Robinson, C. J. & Vaughan, T. M., Brain - Computer Interface Technology: A Review of the First International Meeting. IEEE Transactions on Rehabilitation Engineering, 8, 164-173,2002.

[5] Millan, J. D. R., Ferrez, P. W. & Buttfueld, A., Non Invasive Brain-Machine Interfaces. ESA Ariadna Study 05/6402, ESA Contract 19706/06/NL/HE, 2006.

[6] Lehtonen, J., EEG - Based Brain Computer Interfaces. Department of Electrical and Communications Engineering. HELSINKI University of Technology, 2002.

[7] Inverso, S. A.,  Automatic Error Recovery Using P3 Response Verification for A Brain - Computer Interface. Computer science Department. Rochester Institute of Technology, 2004.

[8] Telpan, M., Fundamentals of EEG Measurement. MEASUREMENT SCIENCE REVIEW, 2, 1-11, 2002.

[9] Tschuor, L., Computer Game Control through Relaxation - Induced EEG Changes. Signal Processing Institute, 1-38, 2002.

[10] Nguyen, C., Brain - Computer Interface. 1-17.www.christinamnguyen.com /BCIfinalpaper.pdf, 2007.

[11] Beverina, F., Palmas, G., Silvoni, S., Pixxione, F. & Giove, S., User adaptive BCIs: SSVEP and P300 based interfaces. PsychNology Journal, 1, 331 – 354, 2003.

[12] Garcia, G., High frequency SSVEPs for BCI applications. Brain-Computer Interfaces for HCI and Games Workshop. Florence, Italy, 2008.

[13] Cheng, M., Gao, X., Gao, Shangkai & XU, D., Design and Implementation of a Brain - Computer Interface With High Transfer Rates. IEEE Transactions on Biomedical Engineering, 49, 1181 - 1186, 2002.

[14] Gao, X., XU, D., Cheng, M. & Gao, S., A BCI - Based Environmental Controller for the Motion-Disabled. IEEE Transactions on Neural Systems and Rehabilitation Engineering, 11, 137-140,2003

[15] Materka, A. & Byczuk, M., Using COMB Filter to Enhance SSVEP for BCI Applications. Proceedings of the 3rd International Conference on Advances in Medical,Signal and Information Processing (MEDSIP '06). Glasgow, UK, 2006.

[16] Piccini, L., Parini, S., Maggi, L. & Andreoni, G., A Wearable Home BCI system: preliminary results with SSVEP protocol. 2005 IEEE Engineering in Medicine and Biology 27th Annual Conference. Shanghai, China, 2005.

[17] Maggi, L., Parini, S., Piccini, Panfili, G. & Andeeoni, G. , A four command BCI system based on the SSVEP protocol. the 28th IEEE EMBS Annual International Conference. New York City, USA, 2006.

[18] Nielsen, K. D., Cabrera, A. F. & Nascimento, O. F. D., EEG Based BCI - Towards a Better Control. Brain-Computer Interface Research at Aalborg University. IEEE Transactions on Neural Systems and Rehabilitation Engineering, 14, 202 – 204,2006.

[19] Friman, O., Luth, T., Volosyak, I. & Gr¨aser, A., Spelling with Steady - State Visual Evoked Potentials. 3rd International IEEE EMBS Conference. Neural Engineering Kohala Coast, Hawaii, USA, 2007.

[20] Gernot R., M¨uller-Putz & Pfurtscheller, G., Control of an Electrical Prosthesis With an SSVEP - based BCI. IEEE Trans Biomed Eng., 55, 1-5, 2008.

[21] Lin, Z., Zhang, C., Wu, W. & Goe, X., Frequency Recognition Based on Canonical Correlation Analysis for SSVEP - Based BCIs. IEEE Transactions on Biomedical Engineering, 53, 2610 - 2614, 2006.

[22] Kluge, T. & Hatrmann, M.,  Phase Coherent Detection of Steady-State Evoked Potentials: Experimental Results and Application to Brain - Computer Interfaces. 3rd International IEEE EMBS Conference on Neural Engineering. Kohala Coast, Hawaii, USA, 2007.

[23] Friman, O., Volosyak, I. & Graser, A.,  Multiple Channel Detection of Steady-State Visual Evoked Potentials for Brain-Computer Interfaces. IEEE Transactions on Biomedical Engineering, 9, 742 - 750, 2007.

[24] Mitra, S. K.,  Digital Signal Processing A Computer- Based Approach, California, McGraw-Hill, 2006.

[25] Lacanette, K. , A Basic Introduction to Filters - Active, Passive, and Switched Capacitor. National Semiconductor Application, 1-22, 1991.

[26] Bell, J., Tunable Multi Notch Digital Filters A MATLAB Demonstration using Real Data. CSIRO ATNF, 1-7, 2000.

[27] Cormen, T., Leiserson, C., Rivest, R. & Stein, C., Introduction to Algorithms, McGraw-Hill Companies, 1990.

# Text boxes

Third Harmonics

Figure 1. Proposed BCI System

Back

Second Harmonics

First Harmonics

60Hz Noise

Figure 9. User has to select Enter button

Figure 1. Proposed BCI System

Result (if found in the file)

Telephone number File

Insert in the file if the record was not found (after entering all digits and selecting enter button)

Add power Supplier Noise 60Hz

Search using LCS algorithm

Detect the maximum frequency

Notch filter to remove 60Hz power supplier noise

Simulate o1, o2 signal of the user selection frequencies

Figure 6. Matching phone number from the file

Table 2. Comparison Between Previous and Current Telephone Keypad BCI System